## Slide 1: Review of Standard IS 2750:1964 and present trends in Scaffolding to cater to demand of Construction Industries - AR/0066
DWAIPAYAN BHADRA, Sc – E
EROL, Kolkata
Discipline – Civil Engineering

## Slide 2: Objective of the Project
To study the usefulness of the standard in the present construction industry and bridging the gap with the requirement of industry.
The review of the standard for necessity of issuance of amendment or revision or withdrawal and replacement by a new standard, keeping in view the current practices in the construction field for greater acceptability of the standard.

## Slide 3: BACKGROUND
Scaffolding is a temporary structure used to support a work crew and materials to aid in the construction, maintenance and repair of buildings, bridges and all other man made structures at heights above the ground. Safety issues are the prime concern for the scaffolding.

## Slide 4: BACKGROUND
In the present scenario, when there is a boom in construction industry and high rise construction is going on everywhere use of scaffolds are getting tremendous popularity as these are easy to erect and can be dismantled immediately after work. The safety aspect of scaffolding along with cost wise economical aspect is essential for both manufacture and users of the material in current scenario.

## Slide 5: BACKGROUND
Safety is long regarded as one of the major concerns in local construction sites.
Construction industry is one of the most vulnerable to accidents. One way of dealing with the safety issues on site is to provide innovative technological solutions to problems. In order to reduce the high accident toll of scaffolding, the scaffolding system shall be improved by adopting advanced technology to raise the level of safety by means of strengthening the materials and improving the design.

## Slide 6: BACKGROUND
Following conclusions may be drawn :
Scaffolding can play a significant role in building repair works, safety of the Labours and materials in construction.
Scaffolding can be easily erected with less energy and less effort.
In recent trends, metal scaffolds are widely used in comparison to bamboo scaffolds due to its durability and safety.
Various special scaffolding is beneficial for reducing accidents on large construction sites.
Various scaffoldings are very helpful, for small as well as large construction projects which should be selected by considering financial level of project.
Adoption of best International practices in the industry along with incorporation of the same in the standard for making the standard contemporary.
Creation of general awareness among the users and manufacturers for use of best methods.

## Slide 7: BACKGROUND
For safety and health point of view, standard and codes should be used by both manufacturers and users after incorporation of good practices and safety aspects in the standard to make it user friendly and help in minimizing hazards.
So it is high time BIS addresses the issue which will benefit the industry and generate revenue for BIS through BIS Conformity assessment scheme.

## Slide 8: IS 2750:1964 Specification for Steel Scaffolding
Scope - This standard lays down the requirements for materials, fabrication and performance of steel scaffoldings constructed with tubes, fittings and/or prefabricated frames, suitable for use in normal building construction work.
1.2 It does not include suspended or slung scaffoldings,
1.3 Scaffoldings constructed with material other than steel are also not covered in this standard.

## Slide 9: IS 2750: 1964
The standard is around sixty years and the date of last amendment is more than 40 years old.
Although scaffolding is used regularly by both in small and large projects the standard has not been revised. It was felt there is a need for review of the standard to incorporate current practices.

## Slide 10: METHODOLOGY
Carry out only feasibility study and submit report based on desktop analysis and review of Indian Standard –
Access International Standards/Technical Regulations / Technical Journal & Papers from Industry/Association and International Journals etc.
Interaction with Industry
Interaction with Manufacturers
Interaction with the organized and unorganized user including traders who are into construction industry.

## Slide 11: Methodology
Due to the Covid 19 pandemic much interaction could not be made with Manufacturers & Industry associations. However interacted with local engineers to know about the latest trends and practices in the industry.
However International Standards and various documents pertaining to the subject was accessed for reference and study purpose. The same has been studied for review of the Indian Standards

## Slide 12: IS 2750: 1964
On review of the standard the following was observed:
Restructuring the standard is required as per current specification standards
The material specification of the components needs to be reviewed as there has been change in grade and specification including incorporation of new materials since its last amendment.
Introduction of new varieties like system/ modular scaffolding for special works. The basic prefabricated frame is only covered in this standard
Review the Design criteria as it is very generic in nature.

## Slide 13: IS 2750: 1964
Further from interaction with industry it was understood:
This item is repeatedly used and reused in the construction field without any sort of “Expiry Date”
No specific guideline to identify or stipulate the life of the material regarding its repeated use. Further any type of Load Testing/Evaluation of results available to check the stability of the system – Any Intermediate Checks
Proper maintenance guidelines including checks and measures before reuse.

## Slide 14: WORK DONE – STUDY OF EXISTING LITERATURE
SAFETY CODES RELATED TO ENABLING WORKS (SCAFFOLDING) – Indian Standards
IS 3696 : Part 1 : 1987 Safety code of scaffolds and ladders: Part 1 Scaffolds
IS 4014 : Part 1 : 1967 Code of practice for steel tubular scaffolding: Part 1 Definitions and Materials
IS 4014 : Part 2 : 2013 Steel tubular scaffolding - Code of practice: Part 2 safety provisions for
scaffolding (First Revision)

## Slide 15: WORK DONE– Technical Documents
A Guide to Scaffold Use in the Construction Industry (OSHA 3150 2002 (Revised) U.S. Department of Labor)
BS-EN-12811-1-British-Standard-Scaffolding-Performance Requirement
BS-EN-12811-2-British-Standard-Scaffolding-Material Requirement
BS-EN-12811-3-British-Standard-Scaffolding-Load Test-Requirement
BS EN 39:2001 - Loose steel tubes for tube and coupler scaffolds — Technical delivery conditions
BS 1139 – Metal Scaffolding (Relevant Parts)

## Slide 16: WORK DONE– Technical Documents
Australian/New Zealand Standard- AS/NZS - 1576.1:2010 - Scaffolding - Part 1: General requirements
CODE OF PRACTICE FOR METAL SCAFFOLDING SAFETY (Labour Dept Govt of Hong Kong)
Scaffolding Code of Practice 2009 (Queensland Government Gazette)
BS EN 74-1:2005 - Couplers, spigot pins and baseplates for use in falsework and scaffolds
NATIONAL ACCESS & SCAFFOLDING CONFEDERATION, UK (Technical Documents)

## Slide 17: STUDY OF THE INTERNATIONAL DOCUMENTS
On study of the International Standards the following is observed which is absent in the existing standard:
Detailed methodology of structural and general design for scaffolds have been given
Guidelines for Erection, dismantlement, movement, and modification of scaffolding
Load Testing requirements and Evaluation of results of scaffold systems
Inspection and maintenance procedures

## Slide 18: The Building and Other Construction Workers' (Regulation of Employment and Conditions of Service) Central Rules, 1998
Review of the existing standards under scaffolding to see if there is any deviation with the current regulations
To see if there is any additional requirement to be incorporated based on this regulation
There is a requirement in the Rules that all metal scaffolds used in building or other construction work conform to the relevant national standards. However no BIS licenses

## Slide 19: Action plan for completing the project – The Way Forward
Review of the standard vis a vis the other international standards and journals
Introduction of a checklist to review the scaffolding system which is now used in many places. To distribute the same to the stake holders for getting a feed back.

## Slide 20: Action plan for completing the project – The Way Forward
In the organized construction sector in most of the cases steel scaffolding used. However there is no license for the product.
Best industry practices may help to bring in Licences
There are now agencies in India who supply scaffolding and formwork as per the requirement of the client. Concept of system and modular scaffolding for special uses.

## Slide 21: Action plan for completing the project – The Way Forward
A good code of practice along with the Product standard may help BIS explore the option of certifying them in line with RMC certification by incorporating the best industry practices. (Like National Access & Scaffolding Confederation-NASC -UK. NASC is the national trade body for access and scaffolding in the UK – established 1945 and now serving a family of 300+ leading contracting firms, scaffolding suppliers and manufacturers)

## Slide 22: TIMELINE
By Mid Nov 20 - To distribute the checklist with the stake holders for their comments
By Dec 20 – Compiling the feedback and review the standards pertaining to the same
By Jan 21 – Submit a PROPOSAL to CED 7 for taking up with the Committee

## Slide 23
THANK YOU