## Slide 1: action research proposal - To study distillation characteristics of kerosene (IS 1459) and petroleum hydrocarbon solvents, (IS 1745)
Nagamani.T,
Sc ‘E’, PCD

## Slide 2: Objective
In IS 1745:2018 Petroleum hydrocarbon solvents- Specification (third revision), Final boiling point of solvent grade 120/240 is specified as 245°C, maximum and is overlapping with that of Kerosene [IS 1459:2018 Kerosene – Specification (fourth revision)], which is 300°C, maximum.
By studying distillation characteristics and finding out the values of 50% and 95% volume recovery temperatures in both standards, differentiating solvent from kerosene will become easy.

## Slide 3: Background….
Regular queries from importers stating
Overlapping of final boiling point of hydrocarbon solvent (120/240), with kerosene
Their product being considered as kerosene as the parameters of solvent is qualifying with that of kerosene, by Customs authorities.

## Slide 4: Background….
IS 1459:2018 Kerosene – Specification (fourth revision)
Prescribes requirements and methods of sampling and test of Kerosene intended for use as an illuminant and as a fuel
IS 1745:2018 Petroleum hydrocarbon solvents- Specification (third revision)
Prescribes the requirements and the methods of test for Petroleum Hydrocarbon Solvents generally used in solvent extraction of oils, rubber and paint industries, in the formulation of insecticides, for dry cleaning and for textile printing purposes

## Slide 5: Background….
IS 1459:2018 Kerosene – Specification (fourth revision)
Requirements in specific to kerosene….
a) Acidity, inorganic;
b) Burning quality; and
c) Smoke point.
IS 1745:2018 Petroleum hydrocarbon solvents- Specification (third revision)
Requirements in specific to 120/240 solvent….
a) Initial boiling point;
b) Aromatic content; andc) Residue on evaporation.

## Slide 6: Overlapping parameters…..
Requirement | IS 1459 Kerosene | IS 1745 Petroleum hydrocarbon solvents
Flash point, ˚C | 35 | 30
Density | To be reported | To be reported
Distillation |  | 
50% & 95% recovery by volume, ˚C | ------ | To be reported
Percent recovered below 200°C, percent (v/v), Min | 20 | ----
Final Boiling point, ˚C | 300 | 240

## Slide 7: Methodology
To compare the test results of the kerosene and solvent 125/240, produced by oil companies during 2019-2020, month-wise
To test around 6 samples, with the help of Committee members, with atleast 2 samples in each laboratory
The data obtained would be analyzed for carrying out necessary modifications / revision of both specifications

## Slide 8: Constraints encountered…..
All oil companies took sometime and have provided data only after repeated reminders
Inspite repeated reminders, Nayara energy and RIL (private oil companies) have not provided data
  They were requested once again during the PCD3 meeting held on 27 October 2020 and they agreed to provide by 2 November 2020

## Slide 9: Progress of work done..
Data provided by IOCL, BPCL and HPCL, for both solvent and kerosene
MRPL provided data only for kerosene
Action Research Project\Kerosene data analysis.xlsx
Action Research Project\Solvent data and Final graph.xlsx

## Slide 10: Action Plan for completing the project
IOCL, BPCL and HPCL representatives agreed to provide samples as well to allow to carry out/ witness testing of distillation and density parameters in their IOCL, Panipat Refinery, BPCL, Bijwasan and HPCL, Badarpura laboratories
To coordinate with IOCL and get the samples tested in the 3 labs, by visiting the facilities, by the end of November 2020
Data correlation, report writing will be completed by the 15 December 2020
Recommendations for amending the requirements, if any, to be discussed in the Subcommittee meetings planned in the end of December 2020.

## Slide 11
Thank You