## Slide 1
Instrumentation in Hydraulic Structures

## Slide 2
1
DAM INSTRUMNETAION
DAM INSTRUMNETAION
NEED OF DAM INSTRUMENTATION
INSTRUMENTATION OBJECTIVES
2
Monitoring
PARAMETERS TO BE MONITORED
SELECTION OF INSTRUMENTS
3
PURPOSE OF DAM INSTRUMENTAION
PURPOSE OF DAM INSTRUMENTAION
PHASE OF DAM INSTRUMENTAION
LEVEL OF DAM INSTRUMENTAION
4
TRIGGER VALUES
TRIGGER VALUES
ELEMENETS OF MONITORING SECHME
PLANNING MONITORING SECHME
WORK FLOW CHART
5
DAMS INSTRUMENTATION
EARTH ROCK FILL DAM
CONCRETE DAM
GEOPHYSICAL METHODS
6
BIS CODES USED IN
DAM INSTRUMENTATION
CODE OF EARTHFILL & ROCKFILL DAM
CODE OF GRAVITY DAM
CODE OF CONCRETE DAM
Table of content

## Slide 3
Instrumentation is the use of special devices to obtain critical scientific measurements of engineered behavior.
Instrumentation consists of the various electrical and mechanical devices used to measure pressure, water flow, movement, stress, strain, temperature etc at a dam and its appurtenant structures.
Symptoms of dam distress can be detected by a monitoring scheme designed with the right instrumentation.
Instruments may operate mechanically, optically, electrically, or via pneumatic or hydraulic principles.
Some instruments are read remotely; others are read at or near their sensors.
The signal may be transmitted by a rod, wire, a liquid column, an electrical/optical cable, light or laser beam, a line-of-sight, or a radio signal.
DAM INTRUMENTAION

## Slide 4
Every structure creates certain risks, and dams are no exception. Most dam failures that have occurred could have been avoided if the structure's behavior had been inspected, monitored, and analyzed continuously.
Structural displacements, deformations, settlements, seepages, the piezometric pressure within the structure and its foundation are items that are the focus of a monitoring system.
Effective instrumentation can play a vital role in the ongoing assessment of a dam's performance, can provide valuable information concerning the safety of the dam, and can help to improve dam design in the future.
NEED OF DAM INTRUMENTAION

## Slide 5
The primary purpose of any structures including dams and appurtenant structures is to develop safe,
cost-effective, and reliable structures.
Instrumentation plays a vital role in assessment and monitoring the changes in any parameter, some of which
are listed below:
Site Characterisation: Parameters of interest are identified depending on the type and function of a
structure
Design verification: To validate the assumptions with actual response of structure and assumed
behaviour to be in close agreement
Construction Control: Mid Way correction based on instrumented data
Quality Control: to enforce the quality of workmanship on a project and to document that work was
done to the specifications
Safety: To issue safety warnings
Legal protection: Used as evidence
Performance: Long-term durability and stability
Instrumentation objectives

## Slide 6
The important parameters to be regular monitoring in Concrete and masonry dams are listed below:
i. Water Level and Pressures
• Reservoir Levels
• Uplift Pressures
ii. Seepage and Leakage
• Seepage through Foundation/Abutment
• Leakage through holes and cracks in Dam Body
iii. Movement
• Surface – Vertical
• Internal - joints and cracks
iv. Stress and Strains
• Stress/strains in concrete structure
v. Temperature (Measured during construction)
• Evaluate mix design
• Placement rates
• Block/lift sizes
• Time of grouting of block joints
• Evaluate thermal loads/stresses
vi. Seismic Loads
• Dynamic Studies/Analysis
PARAMETERS TO BE MONITORED

## Slide 7
While selection of instruments for monitoring for a particular project, the following basic
requirements should be considered:
i. Range: Range is the maximum distance over which the measurement can be performed, with
greater range usually being obtained at the expense of resolution.
ii. Resolution: The resolution is the smallest numerical change an instrument can measure.
iii. Accuracy: The degree of correctness with respect to the true value is the accuracy, and it is
usually expressed as a plus-or-minus number or as a percentage.
iv. Precision: Precision is the repeatability of similar measurements with respect to a mean,
usually reflected in the number of significant figures quoted for a value.
v. Conformance: Conformance is whether the presence of the instrument affects the value being
measured.
vi. Robustness: This is the ability of an instrument to function properly under harsh conditions
to ensure that data accuracy and continuity are maintained.
vii. Reliability: Reliability is synonymous with confidence in the data; poor quality or inaccurate
data can be misleading and is worse than no data.
SELECTION OF INSTRUMENTS

## Slide 8
The primary purpose of instrumentation is to supply data to aid in evaluating the safety of a structure by collecting quantitative data on its performance and by detecting problems at an early and preventable stage
A secondary purpose is to enable comparison of actual behavior with predicted behavior, which verifies design adequacy and helps gather useful information for refining the design of similar structures in the future.
PURPOSE OF DAM INSTRUMENTAION

## Slide 9
DESIGN PHASE
CONSTRUCTION PHASE
FIRST RESERVOIR
FILLING PHASE
OPERATION PHASE
Providing an early indication of unusual performance
Providing confirmation of satisfactory performance
Providing data to understand actual performance
Monitoring the performance to gauge the dam safety
Measuring the impact of various loading conditions.
Instrumentation part of investigations to establish baseline conditions like groundwater profile and for geo-technical monitoring
May be used during construction and further phases to know changes in baseline conditions
  Confirmation of design assumptions
  Changes in groundwater s stability conditions
  Safety and Quality control
PHASES OF INSTRUMENTAION

## Slide 10
Level of instrumentation and frequency of monitoring depends on
Hazard potential of dam
Age or condition of dam
Variation in loading conditions
History of abnormal behaviour
Seismic risk at the dam site
Level of instrumentation and frequency of monitoring may change based on the abnormal performance
LEVEL OF INSTRUMENTAION

## Slide 11
For instrumentation data to be of any value, the instruments must be calibrated and
maintained properly.
Proper care of the equipment is essential to ensure correct readings. Inaccurate readings are worse than no readings at all because they can mislead one about the performance of a dam and can allow serious problems to develop undetected.
Check onsite instrumentation on aregular basis for damage fromweather, traffic, or vandalism.
Follow all manufacturer’sinstructions and guidelines as givenin the operating manuals, including instructions for proper care of the equipment.
MAINTAINANCE & PERFORMANCE
OF INSTRUMENTAION

## Slide 12
TRIGGER VALUES
Tigger values for each parameter being monitored are needed to be defined in the Instrumentation
Plan. This will enable the responsibilities and the action plans for any emergent situation. The trigger
levels may be classified as:
Baseline Level: The observed values fall within expected limits in line with that predicted during
design;
Warning Level: Monitored values exceed the baseline level;
Alarm level: The observed values exceed the warning level
The Baseline, Warning and Alarm levels shall be defined by the Designer. The trigger levels shall be
assigned for each parameter based on the design values and material characteristics. These are
dependent on the type of structure and the geology. For example; the baseline values for anchor loads
may be considered to be satisfied when the measured change in anchor load is within 50% of the yield
strength of anchor. Similarly, warning level may be supposed to have reached when measured anchor
load exceeds 50% of yield strength of anchor and alarm level may be fixed when anchor load exceeds
62.5% of the yield strength.
Similarly trigger levels can be defined for other parameters like pore pressures, uplift pressures,
vertical settlements, horizontal movements, temperature changes, stress/strains, convergences, dam
deflections etc.
TRIGGER VALUES

## Slide 13: Key Elements of Monitoring Scheme
01 | 02 | 03 | 04
Risk knowledge | Monitoring and Warning Service | Dissemination and Communication | Response Capability
Systematically collect data and undertake Risk assessments Are the Hazards and Vulnerabilities well known? What are the patterns and trends? Are risk maps and data available? Deterministic or Probabilistic Analysis? | Develop Hazard Monitoring and Early Warning Service Are the right parameters being Monitored? Is there a sound scientific basis for making forecast? Can accurate and timely warnings be generated? | Communicate Risk information and Early Warnings Do Warnings reach all of those at risk? Are the risks and warnings understood? Is warning information clear and usable? | Build Community Reponses Capabilities Are response plans up to date and tested? Are local capacities and knowledge made use of? Are people prepared and ready to react to warnings?

## Slide 14: Planning a Monitoring Scheme
DESIGN- Risk
knowledge
Understand Project Risk Scenarios
Design Criteria
Choice of Geo- indicators
Calculate trigger
values
Define locations C provide redundancies
01
MONITORING
Instruments Installation
Data Collection
Data Transmission
Data Elaboration
02
Dissemination s Communication
Data Interpretation
Comparison with threshold
Forecasting Methods
Warning
03
EDUCATION-
Response Capability
Risk Perception
Safe Behaviors
Response to Warnings
Population Involvement
04

## Slide 15
No
Yes
Yes
No
No
Carrying out routine monitoring of all instrument as planned
Compile check and analysis data
Any exceedance of alert level
Any exceedance of action level
Notify PMC and Client
Present daily/weekly/monthly report as necessary
Notify PMC and Client
Implement the approved response action and submit report
Inspect affected area and physically monitor the situation
Any exceedance of alarm level
Immediately inform Client, Designer and PMC
PMC notify to Client
Implement emergency actions
Submit interim report to designer and PMC approved report will be sent to Client
Suspend construction works in affected area
Submit report on construction methods full history of movement response actions taken or any other appropriate actions are required
Client approved report, contractor resume work, I&M team include exceedance in monthly I&M team report to PMC and Designer
Incident inspection & emergency review meeting
Response Actions Workflow Chart

## Slide 16: EARTH ROCK FILL DAM
Pore Water Pressure
Seepage/ drainage
  Deformation
  Internal movement
Surface movements
Reservoir and Tail water level
Seismic
Stress and strains
Rainfall
Wave Height and evaporation

## Slide 17
Piezometer
Total Pressure Cell
Settlement Gage
Extensometer/ Inclinometer
Survey Ref. Point
Measurement Weir
Water Level
G
G
e
G G
e e
P
P
P
P
P
P
G
e
P
s
s
s
w
w
G
e
G
e P e
G G G
e e
e
s
C
C
C
C
G
e
P P P P
C C
P P P P P P e P
C
P P P P P P
P P P
P
EARTH ROCK FILL DAM

## Slide 18: Earth s Rock fill dams
Parameter Location | Visual observation | Movements | Uplift and pore pressure | Water levels and flow | Seepage flows | Water Quality | Temperature measureme nt | Crack / joint measureme nt | Seismic measureme nt
U/S slope | ✓ | ✓ | ✓ | ✓ |  |  |  |  | ✓
D/S slope | ✓ | ✓ | ✓ |  | ✓ | ✓ | ✓ | ✓ | ✓
Abutments | ✓ | ✓ | ✓ |  | ✓ | ✓ | ✓ |  | ✓
Crest | ✓ | ✓ | ✓ |  |  |  |  | ✓ | ✓
Internal drainage system |  |  | ✓ |  | ✓ | ✓ | ✓ |  | 
Relief Drain | ✓ |  | ✓ |  | ✓ | ✓ |  |  | 
Riprap and other slope protection | ✓ |  |  |  |  |  |  |  | 

## Slide 19: Concrete dams
Parameter Location | Visual observation | Movements | Uplift and pore pressure | Water levels and flow | Seepage flows | Water Quality | Temperature measuremen t | Crack / joint measuremen t | Seismic measuremen t | Stress-strain measuremen t
U/S slope | ✓ | ✓ |  | ✓ |  |  | ✓ | ✓ | ✓ | ✓
D/S slope | ✓ | ✓ | ✓ |  |  |  | ✓ | ✓ | ✓ | ✓
Abutments | ✓ | ✓ | ✓ |  | ✓ | ✓ |  |  | ✓ | ✓
Crest | ✓ | ✓ | ✓ |  |  |  | ✓ | ✓ | ✓ | ✓
Internal drainage system |  |  | ✓ |  | ✓ |  |  | ✓ |  | 
Relief Drain | ✓ |  | ✓ |  | ✓ |  |  |  |  | 
Galleries | ✓ | ✓ |  |  |  |  |  | ✓ | ✓ | ✓
Sluiceways/ controls | ✓ |  |  | ✓ |  |  |  |  |  | 

## Slide 20: Geophysical Methods for Dam Investigation
Geophysical Methods | Issues and Concerns |  |  |  |  |  | 
 | Concrete Dam |  | Earth Embankment Dams |  |  | Masonry Dams | 
 | Cracks | Degradati on | Water leaks | landslide | Sink holes | Water leaks | Strength
Electrical Resistivity |  |  | Y | Y |  | Y | 
Streaming Potential |  |  | Y | Y |  | Y | 
Georadar | Y | Y | Y | Y | Y | Y | 
Radar Tomography | Y | Y | Y |  | Y | Y | 
Seismic Tomography | Y | Y | Y |  | Y |  | Y
Seismic Refraction |  |  | Y |  |  | Y | Y

## Slide 21: Suggested Frequency of Readings for Specified Instruments
Type of Instrument | During Construction |  | During initial filling | During Period of Operation |  | 
 | Construction | Shutdown |  | Year 1 | Year 2 to 3 | Regular
Vibrating wire piezometers | W | M | W | BiW | M | M
Hydrostatic uplift pressure pipes | W | M | W | W | BiW | M
Porous-tube piezometers | M | M | W | W | M | M
Slotted-pipe piezometers | M | M | W | W | M | M
Observation wells | W | M | W | W | BiW | M
Seepage measurement (weirs and flumes) | W | M | W | W | M | M

## Slide 22: List of IS Codes Related to Earth and rock fill Dam Instrumentation
Indian Standard | Year of Publication | Title
IS: 7356-1 | 2002 | Code of practice for installation, maintenance and observation of instruments for pore pressure measurements in earth dams and rock fill dams, Part 1: Porous tube piezometers
IS: 7356-2 | 2003 | Installation, observation and maintenance of instruments for pore pressure measurements in earth and rock fill dams - code of practice, Part 2: Twin tube hydraulic piezometers
IS: 7436-1 | 1993 | Guide for types of measurements for structures in river valley projects and criteria for choice and location of measuring instruments, Part 1: For earth and rock fill dams
IS: 7500 | 2000 | Code of practice for installation and observation of cross arms for measurement of internal vertical movement in earth dams
IS: 8226 | 2017 | Code of practice for installation and observation of base plates for measurement of foundation settlement in embankments
IS: 12169 | 1987 | Criteria for design of small embankment dams

## Slide 23
Indian Standard | Year of Publication | Title
IS: 12949 | 2013 | Code of practice for installation, maintenance and observation of instruments for pore pressure measurements in earth dams and rockfill dams: Electrical pore pressure cells - vibratory wire type
IS: 6524 | 1972 | Code of practice for installation and observation of instruments for temperature measurements inside dams; resistance type thermometers
IS: 7436-2 | 2019 | Guide for types of measurements for structures in river valley projects and criteria for choice and location of measuring instruments, Part 2: Concrete and masonry dams
IS: 8282-1 | 1976 | Code of practice for installation, maintenance and observations of pore pressure measuring devices in concrete and masonry dams, Part 1: Electrical resistance type cell
IS: 8282-2 | 1996 | Installation, maintenance, and observations of pore pressure measuring devices in concrete and masonry dams - code of practice, Part 2: Vibrating wire type cell
IS: 10334 | 1982 | Code of practice for selection, splicing, installation and providing protection to the open ends of cables used for connecting resistance type measuring devices in concrete and masonry dams
List of IS Codes Related to Earth and rock fill Dam Instrumentation

## Slide 24
Indian Standard | Year of Publication | Title
IS: 10434-1 | 2003 | Installation, maintenance, and observation of deformation measuring devices in concrete and masonry dams - guidelines, Part 1: Resistance type joint meters
IS: 10434-2 | 1996 | Guidelines for installation, maintenance, and observation of deformation measuring devices in concrete and masonry dams, Part 2: Vibrating wire type joint meter
IS: 13073-1 | 2002 | Installation, maintenance, and observation of displacement measuring devices in concrete and masonry dams - code of practice, Part 1: Deflection measurement using plumb lines
List of IS Codes Related to Earth and rock fill Dam Instrumentation

## Slide 25: List of IS Codes Related to Concrete and Masonry Dam Instrumentation
Indian Standard | Year of Publication | Title
IS: 13073-2 | 2000 | Code of practice for installation, maintenance and observation of displacement measuring devices for concrete and masonry dams, Part 2: Geodetic observation - crest collimation
IS: 13232 | 1992 | Installation, maintenance, and observations of electrical strain measuring devices in concrete dams - Code of practice
IS: 14278 | 1995 | Stress measuring devices in concrete and masonry dams - Installation, commissioning and observations - Code of practice

## Slide 26: List of IS Codes Related to Dam Instrumentat in General
Indian Standard | Year of Publication | Title
IS: 1191 | 2016 | Hydrometric determinations -- vocabulary and symbols
IS: 4967 | 1968 | Recommendations for seismic instrumentation for river valley projects
IS: 6532 | 1972 | Code of practice for design, installation, observation and maintenance of uplift pressure pipes for hydraulic structures on permeable foundations
IS: 14248 | 1995 | Guidelines for instrumentation of barrages, weirs
IS: 14750 | 2014 | Code of practice for installation, maintenance, and observation of seepage measuring devices for concrete/masonry and earth/rockfill dams
IS: 14793 | 2013 | Code of practice for installation, maintenance, and observation of the instruments for vibration studies other than earthquakes on Hydraulic Structures and Machines

## Slide 27: List of IS Codes Related to Meteorological Instrumentation
Indian Standard | Year of Publication | Title
IS: 4849 | 1992 | Meteorology - Rain measures - Specification
IS: 5225 | 1992 | Meteorology - Rain gauge, non recording - Specification
IS: 5235 | 1992 | Meteorology - Rain gauge, recording - Specification
IS: 5793 | 2024 | Specification for Aneroid Barometers
IS: 5798 | 1970 | Specification for Mercury Barometers
IS: 5799 | 1970 | Specification for Wind vane

## Slide 28
Indian Standard | Year of Publication | Title
IS: 5900 | 1970 | Specification for Hair Hygrograph
IS: 5901 | 1970 | Specification for Thermograph, Bimetallic
IS: 5912 | 1997 | Specification for Anemometer, Cup Counter
IS: 5924 | 1988 | Specification for Clock Mechanism and Drums for Meteorological Instruments
IS: 5945 | 1970 | Specification for Barograph, Aneroid
IS: 5946 | 1992 | Meteorology - Whirling psychrometer - Specification
IS: 5947 | 1970 | Charts for recording meteorological instruments
IS: 5948 | 1970 | Specification for Thermometer Screens
List of IS Codes Related to Meteorological Instrumentation

## Slide 29
Indian Standard | Year of Publication | Title
IS: 5973 | 1998 | Pan evaporimeter - Specification
IS: 6805 | 1973 | Specification for Assmann Psychrometer
IS: 6806 | 1973 | Specification for Snow gauge
IS: 6871 | 1992 | Wind Equipment - Distant Indicating - Specification
IS: 7243 | 1974 | Specification for Sunshine Recorder
IS: 7244 | 1974 | Specification for Thermometer for Mercury Barometer
IS: 8336 | 1977 | Specification for Thermoelectric Pyranometer
List of IS Codes Related to Meteorological Instrumentation

## Slide 30
Indian Standard | Year of Publication | Title
IS: 8693 | 1978 | Specification for Net Pyrradiometer
IS: 8754 | 1992 | Electrical Anemograph - Specification
IS: 9085 | 1979 | Specification for Correction Slide for Mercury Barometers
IS: 11875 | 1986 | Specification for Diffuse Pyranometer
IS: 11876 | 1986 | Specification for Airmeter
List of IS Codes Related to Meteorological Instrumentation

## Slide 31
Indian Standard | Year of Publication | Title
IS: 12781 | 1989 | Marine Bucket for Sea Surface Temperature Measurement - Specification
IS: 13436 | 1992 | Sensitive Anemometer - Specification
IS: 13448 | 1992 | Meteorology - Thermoelectric pyrheliometer - Specification
IS: 13459 | 1992 | Angstrem pyrheliometer - Specification
IS: 15216 | 2002 | Balloons - Meteorological
IS: 15243 | 2002 | Velocity Scale Set for Meteorological Purposes
IS: 15253 | 2002 | Dew Gauge - Specification
SP 61 | 1994 | General guidelines for automatic weather stations
List of IS Codes Related to Meteorological Instrumentation

## Slide 32
Some of the lessons learnt while dealing with instrumentation and monitoring of dams, slope stability
problems, underground caverns/tunnels and other associated structures are listed below:
• No instrumentation – better than bad instrumentation
• Data once lost is lost forever e.g. deformations in underground excavations
• Keep your eyes and ears open – visual inspections are vital and serves as verification tool even
in case of malfunctioning of instruments
• Small amount of true, accurate, reliable and realistic data far better than large amount of
inaccurate and erroneous data
• Consistency in monitored data needs to be maintained
• Proper identification of instruments and measuring units
LESSONS LEARNT

## Slide 33
Some of the lessons learnt while dealing with instrumentation and monitoring of dams, slope stability
problems, underground caverns/tunnels and other associated structures are listed below:
• Calibration of instruments (wherever possible) and read out units at regular intervals
• Frequency of monitoring to be maintained for true behaviour of instruments
• Correlate data with previous observations and construction activities, or any environmental
of natural factors or disturbances influencing the data
• Proper formats to be adopted for data recording
• Analysis covering overall variation in parameters with respect to original or initial readings and
rate of change of parameters with time
• Improper interpretation may lead to more confusions and complicacies
• Assigning responsibilities at various levels – owner, contractor, analysing agencies
LESSONS LEARNT

## Slide 34
Write to Us
wrd@bis.gov.in